## Slide 1: Proto-cell: status and plans
Collaboration meeting 21.02.2024
Axel Brunold

## Slide 2: The Proto-cell
Volume of 280ml
Equipped with a He level meter
12 pins for electrical connections
indium seal
fill line/capillary
level meter
detector wiring

## Slide 3: First cryo test run (happening right now)
“Empty“ Proto-cell
Goals:
  Verify that the cell is superfluid leak tight
  Check functionality of the level meter
Air
Vakuum

## Slide 9: Level meter
LC circuit
  Coil on top of the cell
  Outer tube and inner rod as the capacitor
Dielectric constant of rising liquid helium increases capacitance
Leads to change in resonance frequency
Can be seen with a network analyzer
outer tube
inner rod
holes to improve fluid response

## Slide 10: What's next ?
Put an MMC into the Proto-cell together with a heater
Test sensitivity of MMC in liquid helium
Check if phonons can be detected
Go to next larger cell
  Test superconducting motors
  Detection of UV-photons
  Search for delayed triplet signal
  ….